Satellite Platforms

mass controll: Ikke nødvendigvis like viktig lenger da man har mindre og mindre satelitter.
Store sats: Mye å si. Sat worth its weight in gold
- To get the mass of the sat into space → rocket equation
Rocket equation: In order to get the sat to speed is dependent on the initial mass and the final mass of the sat. Final mass is initial mass minus the propellant.

1st and 2nd cosmic speeds: 1st = velocity the sat need to orbit just above the earth minus atmosphere and eearth is a perfect sphere. 2Nd =???

Orbit controll: Keep the satelites position and orientation for its purpose
Attitude controll: orientation of the sat in space. In order to keep contact with earth, take pictures, send data etc.
Perturbations(influence orbits/irregularites): ???
Torque on sateliates for attitude controll:
- Gravity-gradient tourque
- Solar radiotan pressure
- Magnetic Tourqe
- Aerodynamic torque

Stabilizing sats:
- Gravity gradient stabilisation
- Spin stab
- Thruster
- Momentum controll
- using wheels to counteract the spin

Antenna usually decoupled from the sat so when the sat spins the antenna will stand still.

Orient the sat in yaw, roll, pitch also precession needs to be controlled.

Sensor detects problems that will need re-orientation/attitude control.

Power Controll: Not the electronics on board, mainly fuel and stuff. Need fuel to correct orbit and position etc. Use solar panels to keep the electronics alive
Solid propellant:
- Simple, reliable, stable. But cant restart or stopped. Used in launches from earth

Liquid propellant:
- Simple, reliable, unstable. Can be stopped and started. Used if you want to correct sat orbit. Also used in launches

Ion propellant:
- Newer/recent propellant. Complicated, reliable, stable. Can be started and stopped. Cant lift off from earth, cuz it has low thrust. It has high specific impules, so it is good for changing spaceships once in space.

Specific impulse = F/(G0*dm/dt)
dm/dt = mass of proppellant over a certain time

Itotal (total impulse) = F *delta t = deltaP

Ispecific = (Itotal deltaT) /g0*(deltam/deltat) = Itot / (g0 * deltam) not finish

Temp controll: Keep the sat operating. Diff parts have diff temp req.

Telemetry: Communications with satelits. Wihtouth this the sat is not worth anything. Telemetry is important. First thing we do is deploying the antenna so we can tlak with the sat.

Mechanical: All mechanical need to operate withouth any problem. Can loose sat if this shit isnt working 100%

Payload: Purpose generally to create revenue